## Slide 1: Advanced Production Decline Analysis (APDA) Blasingame
Shahab Gerami

## Slide 2: Outline
  Modern Production Analysis Methods
  Introduction
  C.P. & C.R. Productions
  Transient Flow & Boundary Dominated Flow
  P.S.S. Equation for Oil Foundation of Advanced Decline Analysis
  What about Variable Rate / Variable Pressure Production?
  Concept of Material Balance Time
  Blasingame Type-curve Analysis

## Slide 3
3
The objective of Production Analysis:
A Reliable Forecast
Modern decline analysis uses production rates and flowing pressures
Reserve evaluation tool that can provide reliable estimates of recoverable reserve and fluid in-place
Practical and economic alternative to well testing for evaluation of skin and permeability
Uses pressure transient theory (mathematics is similar to the well test but the focus is different- long term data not short term transient data)

## Slide 4
What is Advanced Decline Curve Analysis?
Considers rates and flowing pressures
Takes advantage of rate and pressure transient techniques and models
Includes:
  Type curves
  Flowing material balance

## Slide 5
C.P. & C.R. Productions

## Slide 6
Transient
Early-time or Low Permeability
Flow that occurs while a pressure “pulse” is moving out into an infinite or semi-infinite acting reservoir
Like the “fingerprint” of the reservoir
Contains information about reservoir properties (permeability, drainage shape)
Transient Flow & Boundary Dominated Flow
Boundary Dominated
Late-time flow behavior
Typically dominates long-term production data
Reservoir is in a state of pseudo-equilibrium–physics reduces to a mass balance
Contains information about reservoir pore volume (OOIP and OGIP)

## Slide 7
P.S.S. Equation for Oil
Foundation of Advanced Decline Analysis
Applies to constant rate production

## Slide 8
P.S.S. Equation for Oil - in Decline form
Applies to constant rate production

## Slide 10
What about Variable Rate / Variable Pressure
Production? The Principle of Superposition
Superposition in Time:
1. Divide the production history into a series of constant rate periods.
2. The observed pressure response is a result of the additive effect of each rate change in the history.
Example: Two Rate History

## Slide 11
The Principle of Superposition
N - Rate History
f(t) is the Unit Step Response

## Slide 12
Superposition versus Desuperposition

## Slide 13
The Principle of Superposition –PSS Case
Convert multiple rate history into an equivalent single rate history by re-plotting data points at their “superposed” times

## Slide 14
Actual Rate Decline
Equivalent Constant Rate
q
Q
actual time (t)
Q
Concept of Material Balance Time
= Q/q
material balance time (tc)

## Slide 15
Modern Production Analysis Concepts
  Material balance time- Blasingame and Lee (1986)

## Slide 16
Features of Material Balance Time
MBT is a superposition time function
MBT converts VARIABLE RATE data into an EQUIVALENT CONSTANT RATE solution.
MBT is RIGOROUS for the BOUNDARY DOMINATED flow regime
MBT works very well for transient data also, but is only an approximation (errors can be up to 20% for linear flow)

## Slide 17
17
The Pseudo-Steady State Equation for Oil
Material Balance Eq.
Dupuit Flow Rate Formula

## Slide 18
Material Balance Time of Oil Well

## Slide 27
MBE
MBT
P.S.S. Equation on the Basis of MBT

## Slide 28
Function of Material Balance Time
log(q/Dp)
log(material balance time)
Constant Rate
Harmonic Decline
Exponential Decline is made to appear as a harmonic decline
Constant Flowing Pressure

## Slide 29
MBT Shifts Constant Pressure to Equivalent Constant Rate

## Slide 30
Material Balance Time Curve

## Slide 32
Blasingame Dimensionless Decline Flow Rate Curve

## Slide 39
Blasingame Normalized Dimensionless Decline Flow Rate Curve
(according to the solution of constant rate)
Because of the application of material balance time t , the latter part of Fetkovich-Arps type curves is converged to a harmonic decline curve.

## Slide 40
Concept of Rate Integral

## Slide 41
Blasingame Normalized Dimensionless Decline Flow Rate Integral (qDdi ) Curves
This method can effectively reduce the noise of production data, thus facilitating the analysis. The dimensionless decline flow rate integral function qDdi could be given by:
The above equation represents the average value of the production data up to now.

## Slide 42
Concept of Rate Integral

## Slide 43
Blasingame Normalized Dimensionless Decline Flow Rate Integral Curve
(according to the solution of constant rate)

## Slide 45
Blasingame Normalized Dimensionless Decline Flow Rate Integral Derivative Curve
The definition of dimensionless decline flow rate integral derivative q is given below
In the boundary-dominated flow period

## Slide 47
Blasingame Typecurve Analysis
Blasingame typecurves have identical format to those of Fetkovich. However, there are three important differences in presentation:
1. Models are based on constant RATE solution instead of
constant pressure
2. Exponential and Hyperbolic stems are absent, only HARMONIC stem is plotted
Rate Integral and Rate Integral - Derivative typecurves are used (simultaneous typecurve match)
Data plotted on Blasingame typecurves makes use of MODERN DECLINE ANALYSIS methods:
- NORMALIZED RATE (q/Δp)
- MATERIAL BALANCE TIME / PSEUDO TIME

## Slide 48
Blasingame Typecurve Analysis
Comparison to Fetkovich
- Usage of q/Δp and tca allow boundary dominated flow to be represented by harmonic stem only, regardless of flowing conditions
- Blasingame harmonic stem offers an ANALYTICAL fluids-in-place solution
- Transient stems (not shown) are similar to Fetkovich

## Slide 49
Blasingame Method

## Slide 50
Blasingame: Rate (Normalized)

## Slide 51
Blasingame:Integral- Derivative

## Slide 52
Rate Integral: Definition

## Slide 53
Blasingame Type Curves

## Slide 55
Blasingame Typecurve Analysis

## Slide 56
Blasingame Type-curve Analysis Transient Calculations

## Slide 57
Blasingame Typecurve Analysis Boundary Dominated Calculations-Oil

## Slide 58
Blasingame Typecurve Analysis Boundary Dominated Calculations-Oil (Cont,d)

## Slide 59
Blasingame Typecurve Analysis Boundary Dominated Calculations-Gas

## Slide 60
Blasingame Typecurve Analysis Boundary Dominated Calculations-Gas

## Slide 61
Corrections Required for Gas Reservoirs
Gas properties vary with pressure
Formation Volume Factor
Compressibility
Viscosity
For gas wells, compressibility (and viscosity) can not be considered constants at low reservoir pressure
Equation becomes non-linear for gas wells - no longer follows the harmonic decline

## Slide 62
P.S.S. Equation for Oil
Foundation of Advanced Decline Analysis
Depletion term depends on compressibility
Reservoir flow term depends on B and viscosity.

## Slide 63
Not to be confused with welltest pseudo-time which evaluates properties at well flowing pressure.
Evaluated at average reservoir pressure
Corrections Required for Gas Reservoirs

## Slide 64
P.S.S. Equation for Gas
Pseudo-pressure
Applies to constant rate production (and constant compressibility)
Pseudo-time

## Slide 66
(A5.3-1)
(A5.3-3)
(A5.3-4)
(A5.3-5)
Material balance equation for volumetric reservoirs
we use the chain rule as seen in Equation (A5.3-4) below:

## Slide 67
The first derivative in the numerator of Equation (A5.3-5) is simply the derivative of Equation (A5.3-1) with respect to time.
(A5.3-6)
(A5.3-7)
(A5.3-8)
Taking the derivatives, the denominator is simplified to:

## Slide 68
Combining Equations (A5.3-6)-(A5.3-8) and (A5.3-5), we get Equation (A5.3-9).
(A5.3-9)